## Slide 1: Raspberry Pi – GPIO

## Slide 2: Raspberry Pi – GPIO
26 pin connector

## Slide 3: Raspberry Pi – GPIO
PIN-OUT
8 free digital I/O

## Slide 4: Raspberry Pi – GPIO

## Slide 5: Raspberry Pi – GPIO
Some I/O Electrical Parameters |  | 
VIL | Input low voltage | Typical: < 0,54V
VIH | Input high voltage | Typical: > 2,31V
VOL | Output low voltage | Typical: < 0,40V
VOH | Output high voltage | Typical: > 2,40V
IDRV | Intensity drive (single pin) Sink/Source | 2 - 16 mA (2mA step select) Typical: 8mA
IDRV | Intensity drive (all pins) | Maximum: 50mA !!
RUD | Pull Up/down resistor | Typical: 50 KOhm

## Slide 6: Raspberry Pi – GPIO
import RPi.GPIO as GPIO
GPIO.setmode(GPIO.BCM)
GPIO.setup(23,GPIO.IN,pull_up_down=GPIO.PUD_UP)
print("Esperant contacte...")
GPIO.wait_for_edge(23,GPIO.FALLING)
print("Sortint")
GPIO.cleanup()
PYTHON CODE EXAMPLE
provaio.py

## Slide 7: Raspberry Pi – GPIO
Prerequisites:
>sudo apt-get update
>sudo apt-get install python-dev
>sudo apt-get install python-rpi.gpio
PYTHON CODE EXAMPLE

## Slide 8: Raspberry Pi – GPIO
TEST: GPIO23 (pin 16) connects to GROUND (pin 6)